# IMPROVEMENT: MIDI STOP AND CONTINUE
Arpie now detects MIDI STOP and CONTINUE events coming from the external MIDI synch port and will stop playback after a STOP even if the MIDI beat clock continues.

# NEW FEATURE: FORCE TO SCALE
Force to scale is accessible by pressing and holding the SPAN button

SCALE TYPE					OFF-SCALE NOTE ADJUST
Chromatic	Ionian	Dorian	Phrygian	Lydian	Mixolydian	Aeolian	Locrian				Ignore (No Rest)	Mute (Rest)	Flatten	Sharpen	Alternate

Notes output by the arpeggiator are adjusted (if neccessary) to fall on the scale defined by the key root note (see below) and the scale type. Out of scale notes can be skipped (with or without a rest) or sharpened/flattened by 1 semitone to bring them on to the scale. The Alternate mode sharpens and flattens alternate off-scale notes in the arpeggio sequence. Each time the arpeggio is rebuilt the adjustment applied to each note is also toggled. You can force a rebuild by pressing Alternate while the arpeggio is playing. The adjustment is also alternated with each octave in the arpeggio sequence (so in a sequence spanning 2 octaves notes which are sharpened on the first octave are flattened in the second and vice-versa)

Chromatic	C	C#	D	D#	E	F	F#	G	G#	A	A#	B
Ionian	C		D		E	F		G		A		B
Dorian	C		D	D#		F		G		A	A#
Phrygian	C	C#		D#		F		G	G#		A#
Lydian	C		D		E		F#	G		A		B
Mixolydian	C		D		E	F		G		A	A#
Aeolian	C		D	D#		F		G	G#		A#
Locrian	C	C#		D#		F	F#		G#		A#

The scale root note is selected by pressing and holding the SHFT button

SCALE ROOT NOTE
C	C#	D	D#	E	F	F#	G	G#	A	A#	B

GLOBAL OPTIONS					SLIDE
Send Chan Msg	Pass Orig Notes	Pass Orig Chan Msg	Synch To MIDI In	Synch To SYNCH In					Backwards	Forwards	Set Startiung Point